## Slide 1: Req. 3: Introduction to the Electromagnetic Spectrum
1
2
3
4
5
6
Frequency
1 cycle per second
or
1 Hertz
1 second
=
9 Hertz
=
Electromagnetic
Spectrum
Notes: 3 minutes for this slide
[6] If you want to learn about radio, there are a few things you need to learn before anything else. The idea of “frequency” is one we’ll talk about first.
[5] As we’ve shown earlier, even though we can’t “see” radio waves, we often draw them as ripples like these on the screen.
[4] We also have seen that radio waves travel; they’re always in motion.
[3] If we timed the waves you see on the screen, they would end up taking one second to move from the left vertical yellow line to the right vertical yellow line.
[2] We say that the single sweep of the top wave shown is traveling one cycle per second. In radio talk, we give a name to “cycle per second.” We call it a Hertz (named after an old guy who was a radio pioneer); in this instance, “one Hertz.”
[1] If nine cycles go by in one second, we would call that frequency “nine Hertz.”
Ask: What would we call it if a thousand cycles passed by in one second? One million? Seven million? A billion?
SLIDE END

## Slide 2: Req. 3: Introduction to the Electromagnetic Spectrum
1
2
3
4
5
6
7
8
Wavelength
Longer wavelengths
Lower frequencies
Higher energy
1
1
2
3
Lower energy
Shorter wavelengths
Higher frequencies
Notes: 3 minutes for this slide
[8] Now let’s talk about “wavelength.” Radio waves have certain lengths, and it’s very important to understand this. For starters, you can see that the peaks and valleys of these two radio waves are spaced differently.
[7] <stops movement>
[6] We call the distance between two successive peaks the “wavelength” of the radio wave.
[5] Notice that the wavelength of the top wave is longer than that of the lower wave. The wavelength of the bottom is 1/3 that of the top; you can see that three successive peaks fit in the same space as one above.
[4] The longer the wavelength, the lower the frequency.
[3] One interesting thing is that with longer wavelengths and lower frequencies, the amount of energy in the radio wave is lower, too.
[2] Shorter wavelengths result in higher frequencies.
[1] And just the opposite of longer waves, shorter wavelengths present much higher energy; that’s why the “micro” waves in a microwave oven can heat food!
Ask: What would the wavelength be for one Hertz? 186,000 mi. 10 Hertz? 18,600 mi. 100 Hertz? 1,860 miles 1000 Hertz? (1 kHz) 186 mi. 10,000 Hertz (10 kHz) = 18.6 miles
SLIDE END

## Slide 3: Req. 3.a.: Electromagnetic Spectrum
1
2
3
4
5
6
7
300 kHz
3 MHz
1 MHz
2 MHz
3 MHz
30 MHz
10 MHz
20 MHz
30 MHz
300 MHz
100 MHz
200 MHz
300 MHz
3 GHz
1 GHz
2 GHz
MF
HF
VHF
UHF
MEDIUM FREQUENCY
HIGH FREQUENCY
VERY HIGH FREQUENCY
ULTRA HIGH FREQUENCY
Get out
your notes!
Let’s start drawing
the spectrum
Notes: 4 minutes for this slide
[7] Radio frequencies are divided into ranges based on how these frequencies behave in nature. We don’t have time to talk about all of the frequency ranges, but let’s look at a few that relate to some common radio signals.
[6] MF stands for Medium Frequency: This is the group where you’ll find AM radio, marine radio and some ham radio bands.
[5] HF is High Frequency: This group of frequencies is used for short wave broadcasting. Ham radio operators use HF for most international communication.
[4] VHF is Very High Frequency: These frequencies are used for local communication such as broadcast TV, FM entertainment radio, business and ham radio. These frequencies (and higher) are the ones that operate line-of-sight.
[3] UHF = Ultra High Frequency: Used by police, cell phones and ham radio. FRS radio (so-called “Talk-Abouts) lies in this group, too.
[2] Look closely at this chart. It shows that MF includes frequencies from 300 kHz up to 3 MHz. That’s how many of those individual peaks and valleys (cycles) go by in one second.
[1] As we move through each level we can see that frequencies increase ten-fold.
SLIDE END

## Slide 4: Req. 3.b.: Electromagnetic Spectrum
1
2
3
4
3 MHz
30 MHz
30 MHz
300 MHz
300 MHz
3 MHz
300 kHz
3 GHz
HF High Frequency
VHF Very High Frequency
UHF Ultra High Frequency
MF Medium Frequency
30 Hz
300 Hz
300 Hz
3 kHz
3 kHz
30 Hz
3 Hz
30 kHz
SLF Super Low Frequency
ULF Ultra Low Frequency
VLF Very Low Frequency
ELF Extremely Low Frequency
300 kHz
30 kHz
LF Low Frequency
30 GHz
300 GHz
300 GHz
3 THz
30 GHz
3 GHz
EHF Extremely High Frequency
THF Tremendously High Frequency
SHF Super High Frequency
Notes: 2 minutes for this slide
[4] Here again we show the four frequency groups from the last slide.
There are many more frequency groups we’re not going to talk about, but they create an interesting scientific picture of frequencies!
Point out: These frequencies are listed from top to bottom, low to high. That may be confusing, but it’s how radio experts map out these ranges.
[3] There are five groups of frequencies lower than the four we’ve been studying. Some are used for very specialized communication. (Submarines) And there has been some ham radio work in the LF group. The most fascinating point here is that some of these waves travel very well through solid material, like the earth!
[2] There are three frequency groups higher than our four. These are very fascinating for many ham radio experimenters and scientists, and includes satellite, radar, x-rays and beyond. It even includes light!
[1] But overall, our group of four is what’s important to the vast majority of ham radio operators.
SLIDE END

## Slide 5: Req. 3.c.: Radio Services
1
2
3
4
300 kHz
3 MHz
1 MHz
2 MHz
3 MHz
30 MHz
300 MHz
30 MHz
10 MHz
20 MHz
300 MHz
100 MHz
200 MHz
3 GHz
1 GHz
2 GHz
AM Broadcast
160M
Marine
MF
HF
VHF
UHF
Notes: 2 minutes for this slide
[4] Now let’s look closer at our four groups, starting with “medium frequencies.”
[3] Remember the FCC? The FCC assigns a large portion of the bottom end of the medium frequency range for use by AM radio stations. These days, most people listen to AM radio for sports, news and political talk radio. Most of the time, they listen in their cars!
[2] At the top end of the range, we have frequencies set aside for “marine frequencies.” The Coast Guard monitors these frequencies for boaters who might be in trouble. Big ships even use these frequencies!
[1] Right in the middle of the MF range is a space set aside for ham radio. From now on, we’ll show ham radio frequencies in red (with white lettering). Note that hams call this the 160 Meter band.
Ask: Why do you supposed it’s called the 160 Meter Band?
We often refer to bands by their approximate wavelength for these frequencies. Their wavelength is about 160 meters, just over 500 feet between peaks!
SLIDE END

## Slide 6: Req. 3.c.: Radio Services
1
2
3
300 kHz
3 MHz
1 MHz
2 MHz
3 MHz
30 MHz
300 MHz
30 MHz
10 MHz
20 MHz
300 MHz
100 MHz
200 MHz
3 GHz
1 GHz
2 GHz
AM Broadcast
160M
Marine
MF
HF
VHF
UHF
80M
40M
30M
20M
17M
15M
12M
10M
60M
CB
Notes: 2 minutes for this slide
[3] Next comes the High Frequencies, or “HF” as radio operators call them.
[2] There’s a lot we’re not showing here, but we are showing that ham radio has lots of bands throughout this range!
Point out: You can also see that I have identified each of the ham radio segments by their approximate wavelengths.
[1] Ask: How many of you have heard of “CB Radio.” What do you know about it? It used to be very popular, but now is pretty much used by truckers when they’re out on the highway.
For now, that’s as far as we’ll go with the High Frequency group.
SLIDE END

## Slide 7: Req. 3.c.: Radio Services
1
2
3
4
5
6
7
300 kHz
3 MHz
1 MHz
2 MHz
3 MHz
30 MHz
300 MHz
30 MHz
10 MHz
20 MHz
300 MHz
100 MHz
200 MHz
3 GHz
1 GHz
2 GHz
AM Broadcast
160M
Marine
MF
HF
VHF
UHF
80M
40M
30M
20M
17M
15M
12M
10M
60M
CB
6M
2M
1.25M
FM
TV
TV
TV
AVIATION
VHF-
LOW
VHF-
HIGH
WEATHER
Notes: 2 minutes for this slide
[7] Next comes Very High Frequencies, or “VHF.” This is the first frequency group that requires line of sight transmission. That’s why the type of communication is usually “close-in” or the transmitting towers for it are always located as high as possible in the immediate area.
[6] Before cable TV, one of the most important VHF transmission was for television. This broadcasting still takes place, but cable TV is becoming more popular.
[5] The radio in cars usually has this FM band included. While satellite radio has grown in recent years, many still listen to FM on their car radios, and sometimes even at home!
[4] Aircraft pilots communicate with air traffic control in this band of VHF frequencies
[3] “VHF-HI and VHF-LOW” are bands assigned to business and other private (licensed) communications
[2] This little sliver of band is for weather announcements, usually by the National Oceanic and Atmospheric Administration
[1] And of course, there are ham radio bands in here as well (describe)
SLIDE END

## Slide 8: Req. 3.c.: Radio Services
1
2
3
4
5
300 kHz
3 MHz
1 MHz
2 MHz
3 MHz
30 MHz
300 MHz
30 MHz
10 MHz
20 MHz
300 MHz
100 MHz
200 MHz
3 GHz
1 GHz
2 GHz
AM Broadcast
160M
Marine
MF
HF
VHF
UHF
80M
40M
30M
20M
17M
15M
12M
10M
60M
CB
6M
2M
1.25M
FM
TV
TV
TV
AVIATION
VHF-
LOW
VHF-
HIGH
WEATHER
70cm
33cm
23cm
13cm
12cm
TV
CELL PHONES
FRS/GMRS
6
Notes: 2 minutes for this slide
[6] Now for the Ultra High Frequencies, or “UHF”.
[5] Starting off, there are some TV frequencies in this UHF group to add to the prior VHF group.
[4] Now we have the frequencies used for mobile/cell phones. It used to be that a general purpose radio receiver could listen in on these frequencies, but for privacy, the FCC started requiring that manufacturer’s “block” the radio so that you can’t buy a radio anymore that can listen-in on these private phone calls.
[3] Just like the other frequency groups, there are ham radio bands, (we call them “allocations”) throughout the UHF group.
[2] Ask: “How many of you have used an FRS radio? (“Talkabout?”) The frequencies these radios use is in this UHF group
[1] As we’ve said earlier, just because there are “blank spaces” between the frequencies I’ve shown you doesn’t mean they aren’t used. We just wanted to show some of the uses for these frequencies.
SLIDE END

## Slide 9: Req. 3.c.: Radio Services
1
2
300 kHz
3 MHz
1 MHz
2 MHz
3 MHz
30 MHz
300 MHz
30 MHz
10 MHz
20 MHz
300 MHz
100 MHz
200 MHz
3 GHz
1 GHz
2 GHz
AM Broadcast
160M
Marine
80M
40M
30M
20M
17M
15M
12M
10M
6M
2M
1.25M
70cm
33cm
MF
HF
VHF
UHF
23cm
13cm
12cm
FM
TV
TV
TV
TV
60M
AVIATION
VHF-
LOW
VHF-
HIGH
CELL PHONES
WEATHER
CB
FRS/GMRS
WWV
WWV
WWV
WWV
WWV
Notes: 7 minutes for this slide
[2] I want to share one more little detail with you:
Remember our discussion about WWV? It was that signal that I played for you earlier.
[1] You can see that WWV is located at many locations in the MF and HF frequencies, because these are the worldwide shortwave frequencies. Not only does WWV give you accurate time, but it also can let you know how well various radio frequencies are traveling on any given day, since they do vary!
That’s as much of the various assigned frequencies that I’ll show. I don’t want to totally blow you away with everything that is assigned to just these four frequency groups.
Now we’ll give you a few more minutes to finish up your electromagnetic spectrum charts.
SLIDE END