## Slide 1
1
Radio
Merit
Badge
Module A
Notes: Cover Slide w/2 minutes instructor intro 00:00
[1] Instructors:
> Introduce self
  Name, call, years licensed
  Ham radio interests
> Describe how this course will work
  90 minute class
  Station visit/operations
  Less than a 120 minute class
> Hand out and describe how notes forms are to be used

## Slide 2
Instructor Introductions
Name & Callsign
Home Location
Scouting Experience
Favorite Activity in Amateur Radio
Notes: Cover Slide w/2 minutes instructor intro 00:00
[1] Instructors:
> Introduce self
  Name, call, years licensed
  Ham radio interests
> Describe how this course will work
  90 minute class
  Station visit/operations
  Less than a 120 minute class
> Hand out and describe how notes forms are to be used

## Slide 3: Req. 2b.: What is Radio?
These 2 presentations (A&B) are intended to accompany a workbook to be filled out by scouts as we go along, plus a radio tour in the middle where scouts get to talk on the radio.
The slides don’t go linearly through the requirements so watch the requirement numbers in top right corner of each slide.
When a drawing is required, it will be indicated and we’ll stop for you to complete it.
Note Requirement #s
Notes: 0 minutes for this slide 0:00
[1] Basic Class Format Information

## Slide 4: Req. 2b.: What is Radio?
1
2
3
4
5
6
7
B
S
A
Notes: 2 minutes for this slide 2:00
[7] Ask: Have you ever looked closely at the Radio Merit Badge itself?
There are strange little markings around the top of the merit badge, above the “lightning bolts”
[6] The first little group is a dash followed by three dots.
[5] In Morse Code, that’s the letter “B”
[4] The second group is three dots
[3] The letter “S”
[2] Can you guess what the third is?
[1] A dot and a dash for the letter “A”
“BSA”
Morse Code was the first kind of message sent by man using radio waves.
REQUIREMENT 1 END

## Slide 5: Req. 2b.: What is Radio?
1
What is
Radio?
Notes: 1 minute for this slide 4:00
What exactly is “radio?”
SLIDE END

## Slide 6: Req. 2b.: What is Radio?
1
2
Wireless
“Off The Grid”
Communication system, using electromagnetic waves
Radio?
Notes: 1 minute for this slide 5:00
[2] A technical way of describing radio is that it’s a system to communicate, using electromagnetic waves. But that’s kind of a GEEK response!
[1] Many refer to radio as “Wireless”, which it is… Some will say ham radio is “off the grid”, meaning that with only a generator, a radio and an antenna, we don’t need cell towers, power or telephone lines to communicate.
SLIDE END

## Slide 7: Req. 2b. & 7: What is Radio?
1
Radio?
How many radios are in your cell phone?
Notes: 1 minute for this slide 6:00
[1] How many have used one of these? Is it a “radio?” It is wireless, that’s for sure. But in order for it to communicate, it needs the rest of the system, including computers and telephone wires to interconnect the cell phone towers. But there is definitely a part of it that is “radio.” And most of you use it every day!
SLIDE END

## Slide 8: Req. 2b & 5e & 7.: What is Radio?
1
2
3
4
5
6
1
7
Notes: 2 minutes for this slide 7:00
[1] There are up to 7 radios in a modern cell phone, depending on who made it. Cellular service, wifi, Bluetooth, GPS, Near field Communications for things like Apple Pay and Android Pay, and some cell phones still have a Broadcast FM radio receiver and wireless charging which also uses radio waves.
SLIDE END

## Slide 9: Req. 2b.: What is Radio?
1
2
3
4
5
6
1
Lots of things
we use every day
could be considered
forms of radio…
Notes: 1 minute for this slide 9:00
[1] Many everyday items are actually radios in disguise! Can you think of some?
SLIDE END

## Slide 10: Req. 2b.: What is Radio?
1
2
3
4
5
6
Notes: 2 minutes for this slide 10:00
[6] Today we get our entertainment, news and other information over the Internet. The Internet usually makes it to our devices through radio using WiFi
[5] In addition to WiFi, we get information via satellite, another radio method that is very strong.
But radio isn’t just entertainment and information.
[4] We use radio when we operate our mobile phones.
[3] We use radio when we open the garage door remotely.
[2] We use radio when we heat something in the microwave oven.
[1] We even use radio when the EZPass in our car communicates with the gate to charge us the toll and let us through.
SLIDE END

## Slide 11: Req. 2b.: Broadcasting vs. Two-Way Radio
1
One-Way Broadcast vs. Two-Way Radio
Notes: 1 minute for this slide 12:00
[1] Broadcasting is one-way communication.
Usually you can spot a broadcasting antenna; it’s very tall and such antennas are usually located near large population areas.
Everyone can listen-in on their radio to the programming.
Broadcasting is usually operated as a business, where advertisers pay to have their products/services advertised over the air waves.
Two-Way Communication is just that; it’s NOT one-way broadcasting; there are always two (or more) involved
SLIDE END

## Slide 12: Req. 2b.: Broadcast Radio
1
2
One-Way or “Broadcast”
Notes: 1 minute for this slide 13:00
[2] Broadcast radio used to be a major entertainment source before the Internet. Today there are still many good music radio stations, but there are a huge number of talk radio stations such as ESPN.
Usually, a broadcast radio station has one or more studios like this one, with large “boards” (the equipment with all the buttons and knobs) and of course, computers.
[1] Broadcast stations also use large antenna towers like this one, to make sure their signal can reach as many of their intended audience as possible. When there is a hill or small mountain nearby a populated area, you’ll see one or more of these!
SLIDE END

## Slide 13: Req. 2b.: Broadcasting vs. Two-Way Radio
1
Two-Way Radio:
Commercial Radio
Notes: 1 minute for this slide 14:00
[1] Businesses use two-way communication to be more efficient.
Truckers also use two-way radio such as citizens band, or CB.
SLIDE END

## Slide 14: Req. 2b.: Hobby Radio
1
Two-Way Radio for Hobby:
Family Radio Service (FRS)
Notes: 1 minute for this slide 15:00
[1] Many like to use Family Radio Service (FRS) radios when they need to communicate wirelessly such as during Scout campouts.
SLIDE END

## Slide 15: Req. 2b.: Hobby Radio
1
Two-Way Radio for Hobby:
Amateur Radio
Notes: 1 minute for this slide 16:00
[1] Radio as a hobby is very popular.
Probably the single biggest group of hobby radio people is with ham radio operators
There is no minimum age; every one of you in this class could get an amateur radio license.
SLIDE END

## Slide 16: Req. 2b.: Hobby Radio
1
Two-Way Radio for Hobby:
Radio Controlled Vehicles
Notes: 1 minute for this slide 17:00
[1] Another type of hobby radio is Radio Control of cars, boats, drones, & airplanes.
SLIDE END

## Slide 17: Req. 3.: Introduction to How Radio Waves Travel
1
How
Radio Waves
Travel
Notes: 0 minutes for this slide 18:00
[1] How do you think radio waves move from one point to another? What do you think?
SLIDE END

## Slide 18: Req. 3.: Introduction to How Radio Waves Travel
1
2
3
4
186,000 miles per second!
Notes: 1 minute for this slide 18:00
[4] Even though we can’t really “see” radio waves, we often show them as a series of ripple lines like this.
[3] Radio waves actually move.
[2] They move at the speed of light!
Ask: How fast is “the speed of light”?
[1] <186,000 mi/second> or <approx. 300,000,000 meters/second>
SLIDE END

## Slide 19: Req. 3a.: Introduction to How Radio Waves Travel
EARTH
1
Notes: 1 minute for this slide 19:00
[1] The simplest for of radio wave travel is called “line of sight.” You’ll learn later that radio waves called “Very High Frequency” (and higher) depend pretty much on line of sight.
As shown here, someone transmitting radio waves from their location to yours is simply a matter of sending the signal straight across.
Have them draw this image on their work sheet!
SLIDE END

## Slide 20: Req. 3a.: Introduction to How Radio Waves Travel
EARTH
1
Notes: 1 minute for this slide 20:00
[1] This works well unless there is something in the way of the line-of-sight signal, such as a small mountain.
SLIDE END

## Slide 21: Req. 3a.: Introduction to How Radio Waves Travel
EARTH
1
Notes: 0 minutes for this slide 21:00
[1] That’s why you’ll often see antennas on hilltops so that their line-of-sight signal will travel farther!
SLIDE END

## Slide 22: Req. 8a.(5): Repeaters
1
Repeaters
Disco Ball Demo
Notes: 2 minutes for this slide 21:00
[1] We mentioned “repeaters” a couple minutes ago.
An H-T usually doesn’t have enough power for its signals to go a long distance, because things get in the way of the signal.
VHF and UHF radio signals can be easily blocked by an object such as a tall hill, ham operators frequently will install a repeater on top of the hill.
Repeaters will receive the signal from a low power H-T and simultaneously transmit the received signal out to distances much farther than the little H-T could accomplish all by itself. Others who may not have received the signal straight from the H-T WILL receive the retransmitted signal from the repeater!
Repeaters can be connected to the Internet via systems such as Echolink or the Internet Radio Linking Project. <briefly explain>
There are even links created between the repeater and the Internet that allow you to use you lower-power H-T to speak to someone someplace else in the world!
SLIDE END

## Slide 23: Req. 3a: How Radio Waves Travel
EARTH
1
Notes: 1 minute for this slide 23:00
[1] Even if there are no mountains in the way of you line-of-sight signal the curve of the earth will eventually make it impossible for the signal to reach someone far enough around the curve! Line-of-sight signals can “bend” a little, but not for long distances.
That’s where other forms of wireless radio come into play.
SLIDE END

## Slide 24: Req. 3a.: How Radio Waves Travel
NEW YORK CITY
CHICAGO
DENVER
SAN
FRANCISCO
IONOSPHERE
2ND HOP
2ND HOP
SKIP DISTANCE
SKIP
DISTANCE
2ND SKIP ZONE
EARTH
SKIP ZONE
GROUND
WAVES
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Notes: 5 minutes for this slide 24:00
[16] Consider four cities lying along the curvature of the earth, San Francisco, Denver, Chicago and New York City. We’ve already talked about line-of-sight radio waves, and we know they pretty much can’t follow the curve of the earth.
[15] Even some transmitters designed to send radio waves around the earth will throw off ground waves that won’t go very far.
[14] This is where the Ionosphere comes in. The Ionosphere is an interesting invisible cloud of charged particles that surrounds the earth. This is one of the most interesting parts of radio because it has many effects on radio waves.
[13] If I’m in San Francisco, my transmitter and antenna will throw off radio waves at an angle up into the sky.
[12] When my signal enters the Ionosphere, the radio waves bend back down toward the earth as if they were being reflected off a mirror. While the Ionosphere isn’t exactly a mirror, it has a similar effect. My radio waves come back down to earth at approximately the same angle they entered the Ionosphere, and can be detected by someone listening on my frequency near where the waves get close to the ground.
[11] We call this reflection off the Ionosphere “skip” and the total up and down distance is called “skip distance”
[10] What about the people in Denver? People listening on my frequency cannot hear my signal because it has “skipped” over them! We call this area where a signal skips over the “skip zone.”
[9] After the first skip of my signal, it will reflect off the earth and head back out towards the Ionosphere. It will then reflect again off the Ionosphere, heading back down to earth. Here we show that it hits somewhere near New York City, where someone may be listening in.
[8] We call this the “2nd hop” (or 2nd skip) of my signal. My signal has gone all the way from San Francisco to New York City; not possible with line-of-site or ground waves.
[7] And with a second hop, there is a second skip zone. In the case no one in Chicago will hear my signal because it’s travelling too high for their antennas to detect!
[6] The total of both hops is called the “2nd hop skip distance”
There are two other interesting things that can happen with skip:
[5] Let’s say I position my antenna in such a way as to lower the angle my radio waves travel to the ionosphere.
[4] They will reflect back down at that lower angle, making them go much farther like I’m showing here. Now my first skip hop got my signal all the way to Chicago, while on the first try, it didn’t quite go as far.
[3] And on the 2nd hop, this signal travels over New York City to someplace in the Atlantic Ocean (maybe a tropical island?).
[2] Finally, I might position my antenna so that radio waves angle up too sharply.
[1] They will deflect a bit, but they’ll end up going right through the ionosphere into space; no one will hear them (except an alien or possibly an astronaut or satellite!)
SLIDE END

## Slide 25: Req. 3a: How Radio Waves Travel
1
2
3
EARTH
Notes: 1 minute for this slide 29:00
[3] Now let’s look at what really is amazing…
[2] This skip effect can take a radio wave signal all the way around the other side of earth!
[1] What’s really crazy, signals can sometimes skip their way completely around the earth, and I’m able to hear my own signal!
If the instructor has time: At 186,000 miles per second, how long does it take my signal to make one run around the earth? (25,000/186,000 = .134 seconds; a little more than a tenth of a second.
In our illustration here, it would take about .065 seconds to travel half way around the world!.
SLIDE END

## Slide 26: Req. 3a: How Radio Waves Travel
1
EARTH
Notes: 0 minutes for this slide 30:00
[1] Where have we seen this concept before? How about in the fun house when you look between two mirrors. But each time the light bounces, the image is a little less strong.
SLIDE END

## Slide 27: Req. 3a: How Radio Waves Travel
https://www.voacap.com/hf
Notes: 1 min for this slide 30:00
[1] This is what it actually looks like on a 2-D map of the Earth.
Check it out for yourself at www.VOACAP.com
SLIDE END

## Slide 28: Req. 3a: How Radio Waves Travel
1
EARTH
Finish
Drawing!
Notes: 2 min for this slide 31:00
[1] Now finish your drawings for Requirement 2a.
SLIDE END

## Slide 29: Req. 3b.: WWV and WWVH
Precise Time & Radio
1
Notes: 0 min for this slide 33:00
[1] What do we think radio has to do with precision timekeeping?
SLIDE END

## Slide 30: Req. 3b.: WWV and WWVH
1
WWV
Notes: 1 minute for this slide 33:00
[1] What exactly is “WWV?” WWV is the call sign of the United States National Institute of Standards and Technology's (NIST) radio station near Fort Collins, Colorado.
WWV uses high performance antennas to continuously transmit its signal, and can be heard all over the world!
They transmit simultaneously on several frequencies. Their frequencies and time signals are controlled by atomic clocks located in Boulder, Colorado.
SLIDE END

## Slide 31: Req. 3b.: WWV and WWVH
1
WWVH
Notes: 1 minute for this slide 34:00
[1] NIST also operates the very similar radio station WWVH in Kauai, Hawaii, using the same frequencies.
WWV and WWVH make recorded announcements; since they share frequencies, WWV uses a male voice to distinguish itself from WWVH, which uses a female voice.
They also make other recorded announcements of general interest, e.g., the GPS satellite constellation status and severe oceanic weather warnings. By listening to WWV and WWVH we can determine what the ionosphere is doing and how radio waves will propagate off of it.
SLIDE END

## Slide 32: Req. 3b.: WWV and WWVH
1
<Click for WWV audio>
Notes: 1 minute for this slide 35:00
[1] Instructor: In presentation mode, simply click on speaker icon.
It is helpful to have external speakers for this audio
SLIDE END

## Slide 33: Req. 3c.: DX
1
2
1
Notes: 1 minute for this slide 36:00
[1] Ask: Can you guess what the abbreviation “DX” means?
SLIDE END

## Slide 34: Req. 3c.: DX
1
= “DISTANCE”
Notes: 0 minutes for this slide 37:00
[1] DX is shorthand for "distance."
There’s no exact amount of distance defined for DX, but we say DX communication is over great distances using the ionosphere to refract the transmitted radio signal.
DXing is the pursuit of distant stations with the goal of earning various awards.
SLIDE END

## Slide 35: Req. 3c.: DX
1
= “DISTANCE”
DXpedition
Notes: 1 minutes for this slide 37:00
[1] A DXpedition is a trip to operate in a rare DXCC entity, such as one to Scarborough Reef in the South China Sea.
SLIDE END

## Slide 36: Req. 3c.: Local
1
“LOCAL”
Notes: 0 minutes for this slide 38:00
[1] Local radio operation is where the people talking on radios aren’t far from each other. Typically this is less than 100 miles.
SLIDE END

## Slide 37: Req. 1a.: Electrical Safety
1
Safety!
Notes: 1 minute for this slide 38:00
[1] We need to discuss a topic very important to all radio operators: Safety! In radio, safety requires a lot of understanding. We will introduce some common hazards in radio and the most important things to think about:
SLIDE END

## Slide 38: Req. 1a.: Electrical Safety
1
Notes: 0 minutes for this slide 39:00
[1] The part of our body that is most affected by electricity is our heart.
SLIDE END

## Slide 39: Req. 1a.: Electrical Safety
120 volts AC
1
Notes: 1 minutes for this slide 39:00
[1] If we come in contact with the same 120 volts AC you find in your house the electricity will look for a direct path to ground.
SLIDE END

## Slide 40: Req. 1a.: Electrical Safety
120 volts AC
1
Notes: 0 minutes for this slide 40:00
[1] If it’s a really good ground like a puddle of water, there will be a really strong path for electricity, and that path might travel right through your heart!
SLIDE END

## Slide 41: Req. 1a.: Electrical Safety
120 volts AC
0-5 mA
Safe values
0-1 mA
No sensation
1
Notes: 1 minute for this slide 40:00
[1] If only 1/1000 of an amp (1 milliamp) flows through your body when you contact 120 volts, you probably won’t feel it.
Up to 5 milliamps of current flow at 120 volts is considered safe.
SLIDE END

## Slide 42: Req. 1a.: Electrical Safety
120 volts AC
1000mA
Can electrocute 20 adults
50mA
Heart convulsions usually fatal
15-20 mA
Painful shock – inability to let go
0-5 mA
Safe values
0-1 mA
No sensation
1
Notes: 1 minute for this slide 41:00
[1] If you touch 120 volts and 15-20 milliamps flow through your body, it will be a very painful shock; you may not be able to let go because your muscles will be contracted.
At 50 milliamps, your heart will convulse and you will usually die from electrocution.
At 1000 milliamps (1 amp) can electrocute 20 adults at the same time!
SLIDE END

## Slide 43: Req. 1a.: Electrical Safety
120 volts AC
1000mA
Can electrocute 20 adults
50mA
Heart convulsions usually fatal
15-20 mA
Painful shock – inability to let go
0-5 mA
Safe values
0-1 mA
No sensation
15,000 mA
a.k.a. 15A
1
Notes: 1 minute for this slide 42:00
[1] Hopefully, you’ll have respect for a simple home electrical outlet that can deliver 15,000 milliamps or more!
This is also why the TASER doesn’t kill someone. Even though it is very high voltage, it flows only a couple milliamps of current.
SLIDE END

## Slide 44: Req. 1a.: Electrical Safety
1
Notes: 1 minute for this slide 43:00
[1] Whenever you’re working on radio equipment, unplug the equipment first. Leave the “hot” service work to someone who knows good safety practices for doing that work! Unless you know the special precautions necessary when working on energized equipment, don’t do it! Equipment should be turned-off and unplugged when you work on it.
SLIDE END

## Slide 45: Req. 1a.: Electrical Safety
1
Notes: 1 minutes for this slide 44:00
[1] Sometimes it may be necessary to turn the power off at the circuit breaker box. Don’t hesitate to do that, making sure it’s OK with other family members. And never let anyone else turn the power off or on for you. You need to always confirm with your eyes the status of an electric circuit!
SLIDE END

## Slide 46: Req. 1a.: Electrical Safety
1
1
2
3
Notes: 2 minutes for this slide 45:00
[3] Here we show a guy using both hands while working on something involving electricity.
[2] If the surfaces provide a path to ground, the shortest path will be through his chest and heart – not a good thing.
[1] If instead, he puts one hand in his pocket, the shortest path to ground will be down the side of his body, through his leg and then to ground. This can be a very bad shock; it might even knock him out, but it may not kill him. Having electricity go through your chest creates a likely scenario for death.
SLIDE END

## Slide 47: Req. 1a.: Electrical Safety
1
Grounding
Notes: 1 minute for this slide 47:00
[1] One of the most important safety features of your home ham shack is how the station is properly grounded. Being “grounded” may have meant only one thing to you up to this point. Now it means something a lot better and safer!
SLIDE END

## Slide 48: Req. 1a.: Electrical Safety
Earth
Ground
1
120/
240v
Notes: 2 minutes for this slide 48:00
[1] One of the most important safety features of your home ham shack is how the station is properly grounded. Being “grounded” may have meant only one thing to you up to this point. Now it means something a lot better and safer!
Let’s look at how grounding occurs in your home.
There is a heavy duty wire connected between a transformer and your home. This wire carries 120/240 volts.
It also carries a ground wire that is connected to Earth ground near the pole or the underground transformer.
SLIDE END

## Slide 49: Req. 1a.: Electrical Safety
Earth
Ground
Earth
Ground
3
120/
240v
Notes: 1 minute for this slide 50:00
[1] After it attaches to your home, a main power line is routed through the walls to a circuit breaker box.
The box distributes both 240 and 120 volts throughout the home.
Regardless of the circuit voltage, each includes a ground wire that attaches to the circuit breaker box, then routes outside the box to a ground rod. It is the same Earth ground that the power pole or underground transformer is attached to.
SLIDE END

## Slide 50: Req. 1a.: Electrical Safety
2
Earth
Ground
Earth
Ground
1
120/
240v
Notes: 1 minute for this slide 51:00
[2] When you look closely at an electrical outlet, each socket has an individual ground receptacle that is attached to the overall electrical system ground. If you have your own radio shack in the house, your radios will likely have power supplies that use three-prong plugs, so they will be attached to the electrical system’s Earth ground. But that’s not enough!
[1] When you plug in electrical equipment that have three-prong plugs, they become connected to Earth ground if everything is wired correctly and the connections are properly made.
SLIDE END

## Slide 51: Req. 1a.: Electrical Safety
Ham
Shack
Earth
Ground
Earth
Ground
Earth
Grounds
1
120/
240v
Notes: 1 minute for this slide 52:00
[1] Every ham shack should have an additional Earth ground system. A separate wire is run from your operating table down to ground rods you have pounded into the ground from 6 to 8 feet. Most radio shacks need more than one of these ground rods.
As homes are using more and more plastic plumbing, we recommend the hams use separate ground rods unless they know for sure that materials use for piping will in fact be Earth grounded.
SLIDE END

## Slide 52: Req. 1a.: Electrical Safety
1
Electrical Safety Around Radio Equipment
Notes: 0 minutes for this slide 53:00
[1] Here’s some other important safety factors:
SLIDE END

## Slide 53: Req. 1a.: Electrical Safety
1
Notes: 1 minutes for this slide 53:00
[1] A three-prong plug like this is included on most ham radio equipment that plugs into an outlet. The prongs need to be in good shape. The single round prong will connect the radio equipment to the house ground that we’ve already talked about.
Never use a plug that has the ground prong cut off or somehow removed. If equipment came with a three-prong power cord, it was designed to have all three prongs in place. If they are not, you could be exposing yourself to the risk of a serious shock or electrocution!
Sometimes people will use these adaptors to keep from cutting the ground pin, but this can be very hazardous, too! (no ground, etc.)
SLIDE END

## Slide 54: Req. 1a.: Electrical Safety
3
2
1
Notes: 1 minute for this slide 54:00
[3] One comment about Ground Fault Interrupter (GFI) outlets. These are being used more and more in newer home wiring, and they can be installed in older homes, too. They are also a good idea for ham radio shacks.
GFIs will break the circuit much quicker than the circuit breaker in your panel. You could easily die from a shock before the panel breaker would trip, but a GFI trips very rapidly with very little current flow to ground. To do this they have an electronic monitoring circuit that should be tested, and that’s why there is a test button and a reset button.
Some areas now require AFCIs (Arc-Fault-Circuit-Interrupting) breakers. These are located at the breaker panel, and are designed to protect against electrical fires (as opposed to GFIs).
[2] Just press the black button to test. It will trip the GFI if everything is working as it should.
[1] Once you’ve finished testing it, press the red button to activate the outlet. If you don’t press the red button, the outlet will remain “dead” until you do.
SLIDE END

## Slide 55: Req. 1a.: Electrical Safety
1
Notes: 2 minutes for this slide ______ 55:00
Here’s a few more things to think about.
You never want something like this on the left or in the lower right. Not only might you be overloading the capability of one outlet, you might also be exposing yourself to electrical shock with some of these loose connections. A fire could occur here as well.
The picture on the top right shows a two-prong plug being inserted into a two prong outlet. The outlet is ungrounded; the device to which the plug is attached is probably safe without the ground, but the outlet here is the problem. You would not have a proper ground on any device with a three-prong plug!
All radio ham shacks must be using grounded outlets, preferably with Ground Fault Circuit Interrupters!
SLIDE END

## Slide 56: Req. 1a.: Electrical Safety
1
Rooftop Electrical Safety
Notes: 2 minutes for this slide___ 57:00
[1] What all can you find wrong in this picture? Another situation that occurs is when accessing the roof of your home to set up the antenna. You must steer clear of power lines and never have your antenna near such a line!
SLIDE END

## Slide 57: Req. 1a.: Electrical Safety
2
Lightning
Protection
Notes: 0 minutes for this slide 59:00
[2] Now we’ll change the topic to lightning, the scourge of many ham radio operators.
SLIDE END

## Slide 58: Req. 1a.: Electrical Safety
1
https://www.vaisala.com/
Notes: 1 minute for this slide 59:00
[1] Here is a map of the continental United States that shows the density of lightning strokes from 2016-2022.
How many of you live within areas that show on the upper end of the scale (orange, red, dark red)?
(Instructor shows his QTH and comments on his own situation.)
SLIDE END

## Slide 59: Req. 1a.: Electrical Safety
1
Notes: 0 minutes for this slide 60:00
[1] Let’s take a look at a typical ham radio system.
The heart of our system is the radio.
VISUALS CONTINUE ON NEXT SLIDE

## Slide 60: Req. 1a.: Electrical Safety
1
Notes: 1 minute for this slide 60:00
[1] A critical part of our system is the antenna. Our antenna could be a wire, or an expensive tower setup like this one. Some hams will set up their metal rain gutters to serve as an antenna, or maybe even their aluminum flag pole! For this discussion, we’ll use the tower.
Even the power line coming to the house is part of our station system.
ASK: Anybody know what this might be?
Ham radio operators usually have lightning arrestors in their antenna feed lines to theoretically keep a lightning strike from their radios. I say “theoretically” because if we think we can totally control the nature of a lightning strike, that’s giving ourselves too much credit. Lightning arrestors are a good precautionary step with no guarantees. That said, we should have them in our system.
VISUALS CONTINUE ON NEXT SLIDE

## Slide 61: Req. 1a.: Electrical Safety
1
Notes: 1 minute for this slide 61:00
[1] The most important element for safety is our grounding system. This includes not only how we ground our equipment/antennas, but also the geology of the ground itself (damp/dry/hard/soft, etc). We don’t have time to get into this in depth, but the design of our ground system is critical not only for safety, but in many cases for how effective our system is in sending and receiving signals!
VISUALS CONTINUE ON NEXT SLIDE

## Slide 62: Req. 1a.: Electrical Safety
1
Notes: 1 minutes for this slide 62:00
[1] You can see here that this ham operator put a lot of work into making a good ground at the base of his antenna, under the desk, and on the antenna panel.
VISUALS CONTINUE ON NEXT SLIDE

## Slide 63: Req. 1a.: Electrical Safety
1
Notes: 0 minutes for this slide 63:00
[1] Let’s watch what happens (at least theoretically) when lightning strikes our ham radio system.
SLIDE END

## Slide 64: Req. 1a.: Electrical Safety
1
Notes: 1 minute for this slide 63:00
[1] One of the common ways this can happen is when lightning strikes the electrical power lines. Energy from the strike can travel down the line, looking for a ground. It can instantly travel to the nearest ground which in this case could be the grounded entry point into our house.
Another high risk entry point is through our antenna.
The best case scenario is for the energy to travel down the metal tower and into the ground system around the antenna base. Some energy may try to go down the antenna feed line, but if our lightning arrester does the job, it will bypass to ground. (As we said before, there is no guarantee of this!)
SLIDE END

## Slide 65: Req. 1a.: Electrical Safety
1
Notes: 1 minute for this slide 64:00
[1] Now let’s look at what happens if there isn’t a good system ground. If we didn’t have adequate grounding around the antenna base and either didn’t have a good lightning arrester (or the one we had didn’t work), the energy would travel to the nearest ground which likely would be down to (and through) the radio and into the radio station’s ground rod or the building’s ground system. Your radio FRIES in this case, and if you’re near it and touching it, YOU might fry too!
SLIDE END

## Slide 66: Req. 1a.: Electrical Safety
1
Notes: 0 minutes for this slide 65:00
[1] Since there is no good ground at the base of the antenna, the lightning finds the closes path to ground through the radio.
SLIDE END

## Slide 67: Req. 1a.: Electrical Safety
Direct Current Safety
1
Notes: 0 minutes for this slide 65:00
[1] If anyone thinks that power from a direct current (DC) power supply is safe, just look at what happens when you short out a car battery!
SLIDE END

## Slide 68: Req. 1a.: Electrical Safety
1
Direct Current Safety
Notes: 1 minute for this slide 65:00
[1] If anyone thinks that power from a direct current (DC) power supply is safe, just look at what happens when you short out a car battery!
Remember our chart earlier that showed how little alternating current (AC) was required to kill you. 12 volts direct current is much less voltage, and that is one factor, but look at this chart that shows the cranking amps in an automobile battery! In come cases, over a thousand amps!
SLIDE END

## Slide 69: Req. 1a.: Electrical Safety
1
2
Direct Current Safety
Notes: 1 minutes for this slide 66:00
[2] If you short the positive (red) terminals on this high current ham radio power supply with the negative (black) ground terminals, you’ll get the same result as that from a battery and can severely injure yourself and damage the supply beyond repair, let alone the expense associated with buying a new power supply!
[1] Carefully observe the polarity of these terminals. It’s pretty universal that “red” means “positive” and “black” means “negative.” If you ever encounter a supply that isn’t set up with these colors, have second thoughts on whether you should use it!
SLIDE END

## Slide 70: Req. 1b.: Electrical First Aid
1
First Aid
Notes: 0 minutes for this slide 67:00
[1] Time to talk about First Aid regarding radio equipment & electrical work.
SLIDE END

## Slide 71: Req. 1b.: Electrical First Aid
Electric Shock First Aid
Notes: 1 minutes for this slide 67:00
[1] Always make sure the area is safe before assisting others!
Use a wooden stick or pole to remove electrical hazards and/or turn off a breaker if possible.
SLIDE END

## Slide 72: Req. 1b.: Electrical First Aid
Electric Shock First Aid
Notes: 1 minutes for this slide 68:00
[1] Time to talk about First Aid regarding radio equipment & electrical work.
The first thing to always consider is whether it is safe to enter an area.
Check out for indications of electrical hazards and mitigate them before rendering first aid.
Then call emergency services if appropriate.
Then ABCs: Airway, Breathing, & Circulation.
SLIDE END

## Slide 73: Req. 1b.: Electrical First Aid
Electrical Burns
Loose, dry bandages
Look for entry & exit wounds
Treat for shock
Get help / call 911
Do:
Notes: 1 minutes for this slide 69:00
[1] Most often encountered serious injury with radio is electrical burns.
Know the first aid for treating burns: loose & dry bandages.
Get medical help if the burns are serious.
Always look for entry and exit wounds.
SLIDE END

## Slide 74: Req. 1c.: Li-ion Batteries
Li-Ion Battery Safety
Notes: 1 minutes for this slide 70:00
[1] Li:ion batteries are everywhere around us now and have some great advantages over single-use alkali or other rechargeable batteries.
They charge quickly, are lightweight, and can survive thousands of charge cycles.
They are in phones, watches, laptops, and all manner of electronics.
SLIDE END

## Slide 75: Req. 1c.: Li-ion Batteries
Li-Ion Battery Safety
Notes: 1 minutes for this slide 71:00
[1] But Li:ion batteries can be dangerous. If they overheat they can catch fire.
Once a Li:ion battery is burning neither water nor sand can put it out and often you have to just let it burn and move it away from other things if possible.
They also give off toxic gas when burning, so get away quickly if you are around when one catches fire.
SLIDE END

## Slide 76: Req. 6a.: ITU/FCC
1
ITU?
FCC?
Notes: 1 minute for this slide 72:00
[1] Because radio has no boundaries (radio waves don’t stop at borders), the countries of the free world get together and make formal agreements on how radio should be used.
It is up to each country to create their own laws which ensure they abide by the international agreements.
A formal international group has been created to coordinate the agreements between countries.
SLIDE END

## Slide 77: Req. 6a.: ITU/FCC
2
International
Treaty
United States
Radio Law
International
Telecommunication Union
Federal
Communications Commission
Notes: 2 minutes for this slide 73:00
[2] This international group is called the International Telecommunications Union (or “ITU”). The ITU coordinates the agreements in the form of treaties between countries and has headquarters in Geneva, Switzerland.
[1] The agency in the U.S. government which creates and enforces law to help us fulfill the international treaties is called the Federal Communications Commission (FCC).
Nearly all who transmit radio signals for any purpose are required to be registered and licensed by the FCC.
The FCC is the agency that assigns those call signs we talked about earlier in Requirement 1c.
REQUIREMENT 2 END

## Slide 78: Req. 6b.: Call Signs
1
Call Signs
Notes: 0 minutes for this slide 75:00
[1] Call signs are a unique identification for a licensed radio station.
SLIDE END

## Slide 79: Req. 6b.: Call Signs
1
Notes: 1 minute for this slide 75:00
[1] Broadcast radio station call signs are three or four letters such as the FM station above and the television broadcasting stations on the right.
Cable television does not use call signs because their signal does not travel over the airwaves
Call signs are displayed on other radio stations, like the ones on all airplanes.
SLIDE END

## Slide 80: Req. 6b.: Call Signs
1
2
AA - AL
K
KA - KZ
N
NA - NZ
W
WA - WZ
WB8AXP
K2GW
AD4UM
N7QR
WB8AXP
K2GW
AD4UM
N7QR
Notes: 2 minutes for this slide 76:00
[2] Every licensed ham radio operator is assigned a unique call sign.
[1] All U.S. ham radio operators have call signs beginning with AA-AL, K, N or W
SLIDE END

## Slide 81: Req. 6b.: Call Signs
1
WB8AXP
K2GW
AD4UM
N7QR
0 - 9
Notes: 1 minute for this slide 78:00
[1] Each U.S. ham radio operator also has a single number in their call letters, 0-9
SLIDE END

## Slide 82: Req. 6b.: Call Signs
1
Notes: 1 minute for this slide 79:00
[1] The number in our call shows the call sign district where our first license was granted.
(If you move to another district, you keep the same number. You can’t be sure anymore that a person with a certain district number actually lives in that district…) If each one of you passed the requirements for your ham radio license where you lived right now, what would the number be in your call?
SLIDE END

## Slide 83: Req. 6b.: Call Signs
1
Create Your Own Imaginary Call Sign!
Notes: 0 minutes for this slide 80:00
[1] It is very common for ham radio operators to have a custom license plate made for their vehicle, like this one.
SLIDE END

## Slide 84: Req. 6b.: Call Signs
1
Create Your Own Imaginary Call Sign!
Notes: 1 minute for this slide 80:00
[1] <Create Your Imaginary Call Sign>
  Pick K, N, or W, a number, and add your initials
SLIDE END

## Slide 85: Req. 6b.: Call Signs
1
Global Call Signs
Notes: 1 minute for this slide 81:00
[1] There are 308 entities in the world with unique first letters or combinations of letters and numbers in radio call signs called “prefixes”. (Many countries have multiple entities, such as the U.S. with Guam, Puerto Rico, etc.)
SLIDE END

## Slide 86: Req. 6b.: Call Signs
1
Global Call Signs
5R8UI
Notes: 0 minute for this slide 82:00
[1] If I’m operating in my radio station and come across the call letters “5R8UI”, I know that other ham is licensed in Madagascar.
SLIDE END

## Slide 87: Req. 6b.: Call Signs
1
Global Call Signs
PW8S
5R8UI
Notes: 0 minutes for this slide 82:00
[1] If I contact someone with call letters “PW8S,” I know they are licensed in Brazil.
As a ham radio operator, my heart starts beating hard when I make a contact with a another ham from one of these faraway places!
SLIDE END

## Slide 88: Req. 6c.: Phonetic Alphabet
1
Phonetic
Alphabet
Notes: 1 minute for this slide 82:00
[1] Many letters sound similar over the radio.
Weak radio signals and noise might make it difficult to hear voices.

## Slide 89: Req. 6c.: Phonetic Alphabet
1
1
2
B
C
D
E
G
P
T
V
Z
Phil
Bill
Notes: 1 minute for this slide 83:00
[2] The letters B, C, D, E, G, P, T, V or Z might sound the same.
[1] A guy who gives his name “Phil” during a radio transmission is often mistaken for the name “Bill”
An operator for whom English is not a native language may pronounce letters differently, too.

## Slide 90: Req. 6c.: Phonetic Alphabet
1
A
lfa
B
ravo
C
harlie
D
elta
E
cho
F
oxtrot
G
olf
H
otel
I
ndia
J
uliett
K
ilo
L
ima
M
ike
N
ovember
O
scar
P
apa
Q
uebec
R
omeo
S
ierra
T
ango
U
niform
V
ictor
W
hiskey
X
-ray
Y
ankee
Z
ulu
Notes: 1 minute for this slide 84:00
[1] Radio operators use a standardized phonetic alphabet to improve understanding and avoid communication errors.
<Instructor give his own example> Now each of you speak the call you made a couple minutes ago, using the phonetic alphabet words instead of just saying the letters.
SLIDE END

## Slide 91: Req. 8a.(3): Q-signals and Terms
Q-Signals
There are some shortcuts used by radio operators to talk about common radio things.
These start with “Q”.
QRM
QTH
QSY
Notes: 1 minute for this slide 85:00
[1] There is a lot of lingo and terms unique to ham radio.
One group of such unique ham radio “language” are Q-signals or Q-calls.
It is a way to say common things quickly.
SLIDE END

## Slide 92: Req. 8a.(3): Q-signals and Terms
QRM
Q-Signals
1
Notes: 1 minute for this slide 86:00
[1] If a ham is detecting interference caused by some man-made source, whether it’s from another ham or from a powerline, it’s call QRM.
SLIDE END

## Slide 93: Req. 8a.(3): Q-signals and Terms
QRN
Q-Signals
1
Notes: 1 minute for this slide 87:00
[1] There are lots of natural sources of radio interference and noise.
A lightning strike can be detected by hams many miles away.
When noise is generated by nature like this, hams call it “QRN”
SLIDE END

## Slide 94: Req. 8a.(3): Q-signals and Terms
QRP
Q-Signals
1
Notes: 1 minutes for this slide 88:00
[1] If you are communicating with another ham, and he tells you he is “operating QRP”, that means he is using a very low level of power. Most hams that operate portable like you see in this image are operating “QRP”
SLIDE END

## Slide 95: Req. 8a.(3): Q-signals and Terms
QTH
Q-Signals
1
Notes: 1 minutes for this slide 89:00
[1] If someone asks you where your “QTH” is, that means they want to know the location from which you are transmitting.
Most often, a ham’s QTH is their home, but when they operate mobile, wherever they are at the time of the transmission is their QTH
SLIDE END

## Slide 96: Req. 8a.(3): Q-signals and Terms
QSL
Q-Signals
1
Notes: 0 minutes for this slide 90:00
[1] “QSL” is the Q-signal for “I received your transmission OK.”
SLIDE END

## Slide 97: Req. 8a.(3): Q-signals and Terms
Q-Signals
QSL
1
Notes: 0 minutes for this slide 90:00
[1] QSL is also is the name given to a special printed card that you send to another ham confirming that you had a contact with him.
SLIDE END

## Slide 98
Getting Ready to Visit the Station
Notes: 1 minute for this slide 90:00
[1] After this, you’re about to head on over to our radio station to get your time in making a contact. But first, let’s give you some pointers on how to have fun while you’re doing it!
<Instructor: use slide graphics as your talking points>

## Slide 99: Req. 8a.(6): 10-Minute Real or Simulated Contact PREPARATION _
1
Use the K2BSA Operating Card
Listen and call another ham radio station
Talk with another radio station operator
  Relax and have fun
  Give FIRST name ONLY
  Tell where you live
  Describe your school
  Talk about Scouting
Use Q-signals
Log your contact on card
Be prepared to talk about it when you return!
Contact!
Notes: 1 minute for this slide 91:00
[1] You should first interview your host and find out about how they learned radio.
Then you will talk over the radio with another radio operator somewhere in the world.
<Instructor: use slide graphics as your talking points>
SLIDE END

## Slide 100: Req. 8a.(6): 10-Minute Real or Simulated Contact PREPARATION
2026 K2BSA
Contact Card
Notes: 2 minutes for this slide 92:00
[1] Here is an example of a QSL card! Note that it has a bunch of useful “Q” Signals on it, as well as places to log critical information about a contact with another radio user. Be sure to ask your radio helper about it!
SLIDE END

## Slide 101
1
Radio
Merit
Badge
Notes: 94:00